## Slide 1: Bri’s Battery Documentation
7/6/2026-8/13/2026

## Slide 2: State Machine Prototype (C++)
START
grid offset demand
MQTT_INIT
create clients
subscribe to topics
?mqtt_initialized?
Key:
CAPS = state
= action
transition (true/false branch)
?<boolean>? = condition
CHECK_BROKER
check availability of host port
?broker_available?
CHECK_NETWORK
check wifi
?network_ready?
X
X
Connect all components across the network of the IoT through MQTT over WiFi (hotspot)
DATA_WAIT
subscribe for callback waiting
idle
?packet_recieved?
PARSE_MESSAGE
decode payload
determine message type
organize metadata
validate
?message_processed?
X
X
X
RETRY_BROKER (x5)
RETRY_NETWORK (x3)
RETRY_MQTT (x5)
RETRY_SUBSCRIBE (x3)
PARSE_ERROR
X
X
X
X
MQTT_ERROR
NETWORK_ERROR
BROKER_ERROR
SUBCRIBE_ERROR
Pi receives data from ESPs and correlates identifiers to classes/structs
EVAL_CONTROL_PATH
based on message type and metadata route each dataset to paired logic
?control_mode_chosen?
EVAL_CURRENT_STATE
check current stats
compare current readings to boundaries/goal
?current_state_chosen?
(no packet)
(packet)
Battery is commanded based on the current grid demand
APPLY_CONTROL_PATH
set commanded action
validate response
CHARGE,OUTPUT,IDLE,OFF
set commanded action
validate response
?command_enabled?
RESPONSE_ERROR
mark unhealthy unit

## Slide 3: Class vs Struct Data
Total Battery Percentage (SoC)
AC/DC Output On
AC/DC Input Power
AC/DC Output Power
Power Generation
Plug Voltage (V)
Plug Current (A)
Plug Power (W)
Plug Energy (kWh)
Plug Frequency (Hz)
MQTT Status
Uptime
Firmware Version
Wifi-RSSI
IP Address
Serial
Dsp Version
Arm Version
Error Flags
Alarm Flags
ESP32 Uptime
ESP32 Temperature
AC/DC Output Commands
Plug/Relay On/Off Commands
Telemetry Reads
Log Data
Publish MQTT
Connect
Disconnect
Poll Scheduling/Timing
Checks
Detect/Categorize Faults
Retry Failed Connection
User Human Readable Alerts
Save/load Configuration
Notes: encapsulation

## Slide 4: Troubleshooting the ESP to Pi MQTT Bridge Using UART
Command | Result
Serial.begin(<baud>); void loop(){ Serial.println(“<string>”);} | Establishes shared connection transmission speed and tells the UART peripheral to transmit data bytes

## Slide 5: System Inter-Language Coms Prototype:
BLE Network
Python BLE Service:
Encrypted BLE Packets
MQTT Network
JSON
Pi Broker:
MQTT Network
Fleet Organization (topics)
Command Publish/Subscribe
Data Publish/Subscribe
C++ Controller:
config: Constants and parameterized inputs
devices: Topic identification, variable initialization
mqtt_client: Establish MQTT Client and functions
controller: State machine, networking, battery health logic and faults
debug: All prints for easy removal
main: initialize the controller once at startup, then move into the main controller run loop
Go Dashboard:
JSON
JSON

## Slide 6: System Prototype:
BLE Network
Python BLE Actuator:
Encrypted BLE Packets
MQTT Network
JSON
Pi Broker:
Fleet organization (topics)
Command publish/subscribe
Data and telemetry publish/subscribe
C++ Controller:
Tracks data from battery fleet and evaluates health/faults
Takes input grid demand, determines schedule
Sends command packet back to actuator
Go Dashboard:
Displays data
Tracks trends across time
JSON
JSON
Battery Fleet
Local Broker
Remote Management
MQTT Network
MQTT Network

## Slide 7: JSON Parsing (Python, C++, and Go)

## Slide 8: Successful Automated Package Delivery From Python to C++ Through JSON!